Bilateral Cache FSM

All caches start initially in the “Invalid” state. From this state, the cache can receive a request from the processor for either a shared read or an exclusive read. If the cache receives a shared read, then it would transition to “Waiting for Shared Read Reply” after forwarding the request to the directory. However, if the cache receives an exclusive read, it would transition to “Waiting for Exclusive Reply” after forwarding the request to the directory.

In “Waiting for Shared Read Reply,” the cache waits for either type of read replies and transitions depending on which type of read reply it receives. If it receives a nak, it has to resend the shared read request. If the cache receives a shared reply, it would fill the cache with the block and transition to “Shared.” However, if the cache receives an exclusive reply, it would transition to “Clean Exclusive,” instead.

Once in “Clean Exclusive,” the cache can receive an invalidate message from the directory, where it has to reply with an invalidate ack and transition to “Invalid.” In this state, the cache could also decide to evict the block by sending an eviction request to the directory and transitioning to “Clean Exclusive Waiting for Eviction Ack,” where it waits for an eviction ack before transitioning to “Invalid.” Otherwise, the cache can also transition into the “Dirty Exclusive” state when it receives an exclusive read request from the processor.

After arriving in the “Dirty Exclusive” state, several things can happen. The cache can receive an invalidate from the directory, then it would have to transition to “Invalid” and send an invalidate response with the block attached to the directory. If the cache has to evict the block, it would send a writeback request to the directory and transition into “Dirty Exclusive Waiting for Writeback Ack,” where it waits for a writeback ack from the directory before transitioning to “Invalid.” In this state, the cache could also receive a shared read request from the directory, indicating that the cache should transition out of its “Dirty Exclusive” state into the “Shared” state.

Once the cache transitions into the “Shared” state, several transitions could happen. The directory could receive an invalidate message from the directory, indicating that the cache should transition to “Invalid” and send an invalidate ack to the directory. In addition, if the cache has to evict a block in the “Shared” state for any reason, it would send an eviction request to the directory and transition to “Shared Waiting for Eviction Ack.”

After transitioning to “Shared Waiting for Eviction Ack,” the cache has to wait for one of two messages. If the cache receives an invalidate message from the directory, then it means that the eviction request has not arrived at the directory before the invalidate message was sent, so it has to transition to
“Waiting for Nak,” since the directory would send a nak in response to the cache’s eviction request. If this cache received an invalidate, then this cache could not have been the sharer S that the directory chose to read from, since the directory is required to obtain the first read reply from sharer S before sending out its invalidates. Once the cache receives a nak in “Waiting for Nak,” it would send an invalidate ack and transition to “Invalid.” It is also possible for the cache to receive an eviction ack while in “Shared Waiting for Eviction Ack,” where the cache can transition to “Invalid” without doing anything else.

In “Shared,” it is also possible for the cache to receive an exclusive read request from the processor, where it would forward the request to the directory and transition to “Waiting for Exclusive Read Reply.” In this state, the cache can receive a nak from the directory, telling the cache that the directory is busy and that it should resend its request. Only the exclusive reply message from the directory will transition the cache out of this state and into the “Dirty Exclusive” state.