BENCHMARKS

  -mM : M = even integer; 2**M total complex data points transformed.
  -pP : P = number of processors; Must be a power of 2.
  -nN : N = number of cache lines.
  -lL : L = Log base 2 of cache line length in bytes.
  -s : Print individual processor timing statistics.
  -t : Perform FFT and inverse FFT. Test output by comparing the
        integral of the original data to the integral of the data that
        results from performing the FFT and inverse FFT.
  -o : Print out complex data points.
  -h : Print out command line options.

a typical parameter could be -m10 -p2 -n65536 -l4

Benchmark	Runtime	L1Cache ReadHit	L1Cache ReadMiss	L1Cache WriteHit	L1Cache WriteMiss	L2Cache / ReadHit	L2Cache ReadMiss

fft sodir moesi	137302	115825	10744	78690	2843	13608	11133
fft sodir msi	137189	115822	10761	78718	2836	13620	10843

Table 1 Results for fft with 32 processors
------------------------------------------------------------------------
3.2 Main Memory
In the simulator, the main memory is simulated as a node in the network. Therefore, when a directory wants to request something from main memory, it sends a messages across the network to the main memory. This design simplifies the design of the memory while still keeping the protocol intact.
-----------------------------------------------------------------------------------------
Write down bullet points of my work in top-down fashion
1. What the current status is in my field
2. What the problems are in the current field
3. What is my solution

  1. I set cache size for 1MB because it was close to current processors
  2. -----------------------------------------------------------------------------------------
1. Results Section
    1. I used Sesc with these modifications
-----------------------------------------------------------------

3.1 Network

The underlying network in use for this simulator is a simple black box model. It does not model a real network with routing. Instead it models messages going in and out of the network using a random delay with a lower-bound of 4 and an upper-bound of 20. When more messages arrive, the delay coming from the random delay generator will be shifted higher as to model the higher traffic conditions.

We could have used a more complicated network, one that simulates router-router connection and uses routing protocols, but such a network was not available at the time in the simulator, and the black box network serves its purpose for delivering messages to and from all the directories, as well as the main memory. Although the SESC simulator has the capability to model a more complicated network, a simple network, such as the one used here, can illustrate our point.

In the simulator, we make sure that whenever a message is being sent to a remote node that has the same node ID as the current node, we send the message to itself. For example, if processor 1 requests a block A, where processor 1 is block A's home node, sending a network message from a node to itself it pointless and just results in needless network traffic. We perform a check to see if the destination for a message is the same as the source of the message, previous to sending the network message. If this is the case, it just forwards it straight on to the function that would handle it on the local directory node rather than emitting something on the network.
-----------------------------------------------------------------------------------------------------------------

Comparison Between Architecture of Unoptimized and Origin Systems
However, the importance of the simulation is placed on the extra packages that we are sending. Even in this system, there are still two bilateral interactions for most transactions that needs to be done in the Unoptimized protocol. So the location of the main memory does not affect the simulation that much.

Here I will introduce the layouts of the two architectures that I will be comparing. The two different architectures are very similar because most of the components are connected in the same way. The components themselves are the same, it is only the connections that are different.