Bilateral Directory FSM

The directory for any address will start in the “Unowned” state initially. When the directory receives a read request, it would set the owner to be the requester, forward the request to the memory node, and transition to “Exclusive Waiting for Reply.” In that state, the directory has to wait for a reply from the memory node before it can do anything else, so any read requests that arrive gets nakked. No writeback requests can arrive in “Unowned” because no node has the block, yet. When it receives a reply from the memory node, an exclusive reply is sent to the requester, and the directory transitions into the “Exclusive” state.

From the “Exclusive” state, there are a myriad of situations that can occur. The first can happen when an exclusive read request arrives at the directory and the requester is the owner. The directory has to send a read ack (no data) to the requester when this happens. The second can happen when a writeback request is emitted from the owner. In this case, the directory will clear the owner list, send the write to memory, send a writeback ack to the requester, and transition to “Unowned.” The third is when the directory receives an eviction request in this state. The directory is required to send an eviction ack to the requester, clear the owner list, and transition to “Unowned.” It is not necessary to write to memory in this case, because an eviction request indicates that the message came from a cache whose state was “Clean Exclusive.”

Another type of transition that occurs from the “Exclusive” state is when the directory receives an exclusive read and the requester is not the owner. In this situation, the directory would set the owner to be the requester and send an invalidate to the previous owner, while transitioning to “Waiting for Invalidate Response,” where it waits for a writeback request or an invalidate ack to cause it to transition back to “Exclusive.” If a read request arrives while the directory is in “Waiting for Invalidate Response,” the directory would send a nak to the requester. If the directory receives a writeback request, the directory would send an exclusive reply to the new owner and a writeback ack to the requester. On the other hand, if the directory receives an invalidate ack, it would only send an exclusive reply to the new owner.

It is also possible to transition from the “Exclusive” state to “Exclusive Shared Waiting for Reply” when the directory receives a shared read. This shared read has to come from a requester that is not the owner. The directory has to forward the request to the previous owner, and set the requester as a sharer. In “Exclusive Shared Waiting for Reply,” several things can happen. If the directory receives a shared read in this state, it would add the requester into the sharers list, and if it receives an exclusive read, it would send a nak to the requester. If, it receives a writeback request arrives from the previous owner, then the directory would set the owner to be the read requester, send a writeback ack to the writeback requester, send an exclusive read reply to the read requester, and transition back to “Exclusive.” If, instead, it receives a read reply from the previous owner, then the directory would forward shared replies to all requesters and transition to “Shared.”

In the “Shared” state, if the directory receives an eviction request from a sharer and there are more than two sharers, then the directory would simply remove the requester from the sharers list and send an eviction ack to the requester. If the directory receives a writeback request and the size of the sharers list is 2, then the directory would set the owner to the remaining sharer, clear the sharers list, send an eviction ack to the requester, and transition to “Exclusive.”

When a shared read arrives in the “Shared” state, the directory would add the requester into the sharers list, forward the request to a sharer S, and transition to “Shared Waiting for Reply.” Sharer S is chosen randomly among all the nodes that has the block. In this state, the directory adds any new shared requesters into the sharers list and naks any exclusive reads and eviction requests that are not from sharer S. If the directory receives a shared reply from sharer S in this state, it would send shared replies to all requesters. However, if an eviction request from sharer S was received, then the directory would send shared replies to all requesters, send an eviction ack to the eviction requester, remove the eviction requester from the sharers list, and transition back to “Shared.”

While in “Shared” state, it is also possible to receive an exclusive read request. This request causes the requester to be set as the owner, a transition to “Waiting to Send Invalidates,” and the request to be forwarded to a sharer S, which is chosen randomly among the available sharers. In the “Waiting to Send Invalidates” state, if the directory receives an eviction request not from sharer S, it would send a nak to the requester. If the directory receives a read request in this state, it would send a nak to the requester. If a read reply arrives from sharer S, the directory would send invalidates to all sharers and transition to “Waiting for K Invalidates, J Invalidates Received So Far,” where K is the number of invalidates sent, and J is the number of invalidate acks received so far. However, if an eviction request from sharer S arrives, then the directory would remove the requester from the sharers list, send invalidates to the remaining sharers, send an eviction ack to the requester, then transition to “Waiting for K Invalidates, J Invalidates Received So Far.”

The directory’s primary purpose is to wait for invalidate acks in “Waiting for K Invalidates, J Invalidates Received So Far.” If a read request or an eviction request was received, the directory has to send a nak to the requester. If an invalidate ack was received, the directory checks if J (the number of invalidate acks received so far) is equal to K (the number of invalidates sent). If they are not the same, then the directory continues to wait in this state. However, if J = K, then the directory would send an exclusive reply to the requester.