The (remoteNode == nodeID) check in these places [and you'll see a similar check in a few places] is done to prevent an access where the sending node is also the home node or destination node, from emitting a network message addressed to itself.

BENCHMARKS

  -mM : M = even integer; 2**M total complex data points transformed.
  -pP : P = number of processors; Must be a power of 2.
  -nN : N = number of cache lines.
  -lL : L = Log base 2 of cache line length in bytes.
  -s : Print individual processor timing statistics.
  -t : Perform FFT and inverse FFT. Test output by comparing the
        integral of the original data to the integral of the data that
        results from performing the FFT and inverse FFT.
  -o : Print out complex data points.
  -h : Print out command line options.

a typical parameter could be -m10 -p2 -n65536 -l4

One of the bugs that was extermely hard to find was one caused by various interactions within the system. To decrease the number of messages sent, it is possible for the block allocator in MOESI Cache to allocate a block as soon as it is evicted. Normally, when a block is evicted, the system will undergo this cycle:
1. An OnLocalRead gets called, and AllocateBlock puts tag1 into pendingEviction.
2. OnLocalInvalidateResponse gets called, and removes tag1 from pendingEviction, doing the necessary cleanup.

However, it is possible for the system to undergo the following cycle, especially when faced with a larger number of invalidates and evictions:
1. An OnLocalRead gets called, and AllocateBlock puts tag1 into pendingEviction.
2. Another OnLocalRead gets called before OnLocalInvalidateResponse gets called, and PrepareFreshBlock finds the same tag1 inside pendingEviction. So it cancels the eviction and prepares that block for use.
3. OnLocalInvalidateResponse gets called for tag1, but it cannot find tag1 inside pendingInvalidate or pendingEviction because pendingEviction.erase(tag1) was called during PrepareFreshBlock.

Benchmark	Runtime	L1Cache ReadHit	L1Cache ReadMiss	L1Cache WriteHit	L1Cache WriteMiss	L2Cache / ReadHit	L2Cache ReadMiss

fft sodir moesi	137302	115825	10744	78690	2843	13608	11133
fft sodir msi	137189	115822	10761	78718	2836	13620	10843

Table 1 Results for fft with 32 processors
fft ogdir moesi	1123774	104129	6225	72332	7978	14203	12478	0	0
fft ogdir msi	1125149	104129	6221	72332	7977	14198	12479	0	0
fft sodir moesi	1115194	104123	6228	72331	6898	13125	11396	0	0
fft sodir msi	1150388	104129	6219	72331	6898	13116	11396	0

Table 1 fft with 2 processors
fft ogdir moesi	498957	104907	6332	72760	5226	11559	9742	0	0
fft ogdir msi	497389	104907	6315	72763	5226	11545	9732	0	0
fft sodir moesi	497844	104907	6325	72765	4141	10466	8652	0	0
fft sodir msi	524816	104907	6328	72765	4177	10507	8660	0

Table 2 fft with 4 processors
fft ogdir moesi	286050	106467	6521	73628	3852	10373	8030	0	0
fft ogdir msi	288279	106467	6513	73628	3871	10384	8052	0	0
fft sodir moesi	284774	106464	6509	73628	2939	9450	7105	0	0
fft sodir msi	296535	106465	6557	73629	2937	9495	7248	0

Table 3 fft with 8 processors
fft ogdir moesi	174171	109589	8079	75361	3035	11128	8352	0	0
fft ogdir msi	175160	109589	8094	75361	3032	11142	8339	0	0
fft sodir moesi	171948	109584	8121	75357	2698	10833	7937	0	0
fft sodir msi	173780	109585	8111	75358	2692	10818	7953	0

Table 4 fft with 16 processors